## Slide 1: 加工後刀腹磨耗最大值
2022全國智慧製造大數據分析競賽_ProjectB
隊名：Geek 極客
隊員：林祥憲、鄧修奇、傅家芸
指導老師：鍾禎元 教授

## Slide 2: 目錄
題目說明
方法流程
訓練結果

## Slide 3: 題目說明
數據(CSV)包含了三把智慧刀把於每層加工後的，刀腹磨耗最大值以及每層加工各時間點之加工資訊。
實驗目的：使用三把智慧刀把紀錄相關加工資訊，預測當層加工後刀腹磨耗最大值。
問題屬性：迴歸分析
Train1，train2，test 之資料夾個別存放智慧刀把的加工資訊。
Train1 一共 46 層，train2 一共 24 層，而 test 一共 25 層。
資料夾內分別有00_Wear_data，n_sg，n_spike，三種命名格式的 CSV 檔。

## Slide 4: 題目說明
00_Wear_data (每層加工磨耗最大值為累加)
  欄位 A: 層數編號
  欄位 B: 當層刀腹磨耗最大值

## Slide 5: 題目說明
檔尾為_sg 檔案為伺服資訊
  欄位 A: 時間資訊 (秒)
  欄位 B~I: 伺服資訊(特徵欄位)
檔尾為_spike 檔案為智慧刀把資訊
  欄位 A: 時間資訊 (秒)
  欄位 B~D: 刀把資訊(特徵欄位)

## Slide 6: 方法流程
載入資料
資料前處理
特徵工程
特徵選取
模型訓練

## Slide 7: 載入資料
利用 pandas.read_csv 載入資料
# Read file and seperate each feature to do data preprocessing print('Reading sg...') sg = [pd.read_csv('train1/' + str(i) + '_sg.csv') for i in range(1, 47)] print('Reading spike...') spike = [pd.read_csv('train1/' + str(i) + '_spike.csv') for i in range(1, 47)] print('Reading MaxWear...') output = pd.read_csv('train1/00_Wear_data.csv').loc[:, 'MaxWear']

## Slide 8: 資料前處理
#Seperate each feature to do data preprocessing s = time.time() print('B...', end='') sg_B = [i.values.T[1] for i in sg] print('cost time: ', time.time() - s)
# If the number of data in one column is smaller than maximum, we'll use the last value of that column # to fill in to get a same dimension in one feature(column) s = time.time() print('B...', end='') for i in range(len(sg_B)): if sg_B[i].size < max_num: sg_B[i] = np.append( sg_B[i], [[sg_B[i][-1]] * (max_num - sg_B[i].size)]) print('cost time: ', time.time() - s)
# Change in sg --> change the data from absolute coordination to relative coordination (distance in each timestep) s = time.time() print('B...', end='') CISG_B = [np.array([i[j]-i[j-1] for j in range(1, len(i))]) for i in sg_B] print('cost time: ', time.time() - s)
將每個特徵分開
若數據列數小於最大值，則用最後一列來填充。獲得相同維度的特徵值。
將n_sg絕對座標轉換成相對座標（每單位時間的位移）

## Slide 9: 資料前處理
轉換n_spike資料頻率 A = 0.001, 0.002, 0.003
# Calculate B's, C's, D's values at A = 0.001, 0.002, 0.003..... s = time.time() print('B...', end='') for i in range(len(B)): index = range(3, spike_B[i].size-1, 5) value = [(B[i][j-1] + B[i][j])/2 for j in index] B[i] = insert(B[i], index, value) print('cost time: ', time.time() - s)
# Change in spike --> change the data from absolute coordination to relative coordination (distance in each timestep) s = time.time() print('B...', end='') CISP_B = [np.array([i[j]-i[j-1] for j in range(1, len(i))]) for i in B] print('cost time: ', time.time() - s)
將n_spike絕對座標轉換成相對座標（每單位時間的位移）

## Slide 10: 特徵工程
# Sum up the distance that process during one timestep 0.001 # final_abs_: total path s = time.time() print('B...', end='') final_abs_B = [[abs(CISP_B[j][i*3+1:i*3+4]).sum() for i in range(0, CISG_B[j].size-1)] for j in range(len(CISP_B))] print('cost time: ', time.time() - s)
# fianl_: distance s = time.time() print('B...', end='') final_B = [[CISP_B[j][i*3+1:i*3+4].sum() for i in range(0, CISG_B[j].size-1)] for j in range(len(CISP_B))] print('cost time: ', time.time() - s)
以0.001秒為步長累加n_spike路徑長
以0.001秒為步長累加n_spike位移

## Slide 11: 特徵工程
s = time.time() print('BCD abs Distance...', end='') BCD_abs_distance = [[pow(pow(final_abs_B[j][i], 2) + pow(final_abs_C[j][i], 2) + pow(final_abs_D[j][i], 2), 0.5) for i in range(len(final_abs_A[j]))] for j in range(len(final_abs_A))] print('cost time: ', time.time() - s) BCD_abs_distance = np.array(BCD_abs_distance)
假設n_spike特徵BCD為刀具移動時的XYZ軸，以0.001秒為步長計算刀具總路徑長
s = time.time() print('BCD Distance...', end='') BCD_distance = [[pow(pow(final_B[j][i], 2) + pow(final_C[j][i], 2) + pow(final_D[j][i], 2), 0.5) for i in range(len(final_A[j]))] for j in range(len(final_A))] print('cost time: ', time.time() - s) BCD_distance = np.array(BCD_distance)
s = time.time() print('BDF Distance...', end='') BDF_distance = [[pow(pow(sg_B[j][i], 2) + pow(sg_D[j][i], 2) + pow(sg_F[j][i], 2), 0.5) for i in range(len(sg_B[j]))] for j in range(len(sg_B))] print('cost time: ', time.time() - s) BDF_distance = np.array(BDF_distance)
假設n_spike特徵BCD為刀具移動時的XYZ軸，以0.001秒為步長計算刀具位移
假設n_sg特徵BDF為刀具移動時的XYZ軸，以0.001秒為步長計算刀具總位移

## Slide 12: 特徵選取
work_B = [[1 if abs(sg_B[i][j]) >= 0.0029 and abs(sg_B[i][j]) <= 0.0041 else 0 for j in range(len(sg_B[i]))] for i in range(len(sg_B))] spike_abs_B_lower_noise = spike_abs_B * work_B spike_B_lower_noise = spike_B * work_B
↑ 觀察n_sg、n_spike的B特徵，得出sg絕對值在0.0029至0.0041間是可能的雜訊。

## Slide 13: 特徵選取
假設n_spike 特徵BCD為刀具移動時的XYZ軸，則可將這3個特徵視為與磨耗最大值，相關係數最高的特徵。

## Slide 14: 訓練模型
model = Sequential() model.add(Dense(128, activation='relu', input_dim=Input_shape)) model.add(Dense(4, activation='relu')) model.add(Dense(1)) model.summary() learning_rate = 0.0005 batch_size = 15 epochs = 500 # Adam RMSprop model.compile(optimizer=tf.optimizers.Adam( learning_rate=learning_rate), loss=rmse) history = model.fit(input_train, output_train, validation_data=(input_test, output_test), batch_size=batch_size, epochs=epochs, verbose=1)
Model: "sequential_0" _________________________________________________________________ Layer (type) Output Shape Param # ================================================================= dense_6 (Dense) (None, 128) 768 dense_7 (Dense) (None, 4) 516 dense_8 (Dense) (None, 1) 5 ================================================================= Total params: 1,289 Trainable params: 1,289 Non-trainable params: 0 _________________________________________________________________

## Slide 15: 訓練結果
Test RMSE:
Train RMSE:
Total RMSE: